## Slide 1: QSE to FMC + Displayport Adapter Board
Alex Blate
March 2015

## Slide 2: System Block Diagram
TI 4100 DLP Board
Virtex 5
QSE Connectors
EXP1/EXP2
32 * 2 Diff.
14 * 2 SE
2 * 2 Diff. Clocks
2* 2 SE Clocks
2V5, 3V3, GND
Adapter Board
EXP1/2
(L1/Top)
FMC-HPC
Displayport
(J200)
4 Lanes
JA1 (L16/Bottom)
AUX
Redriver & Level Conversion
Mating Connectors
HTG-777 Board
Virtex 7
Cable
FMC-HPC

## Slide 3: Adapter Board Block Diagram
Adapter Board
EXP2
FMC-HPC
JA1
SN75DP130
Redriver,
Equalizer
32 * 2 Diff.
14 * 2 SE
2 * 2 Diff. Clocks
2* 2 SE Clocks
2V5, 3V3, GND
EXP1
VCC_EXP2_3V3
JP300 JP301
J302
External 3V3 IN
JP301
Option to isolate
DP Power Supply
Input Protect
+3V3
Filter
3V3_RX
Lin. Reg
+1V8
DP IN
3V3_RX
SN74GTL2010
High-speed
Logic level converter
4xLanes
+1V8
+3V3
AUX
3x TPD4S010
ESD Protection
Power Source Select
J100/J101 Ref Clk In (SMA)

## Slide 4: Electrical Parameters -- Power
Active components powered from VCC_EXP2_3V3 or external 3V3
  No active on-board power supply/regulation.
  3V6 3W Zener + 500mA PTC fuse
  Reverse voltage protection diodes
Ferrite filters + caps on input rails
Highly-filtered but non-isolated 3V3_RX rail to power SN75DP130
Common ground throughout board
All other power supply inputs (from QSEs) decoupled to GND
ESD Protection on connected DP pins
DP PWR_OUT pin not connected; RTN_PWR tied to GND

## Slide 5: Digital Signaling
Differential Lines
  Designed for ~100 Ohm diff. impedance
  Microstrip: 5mil at 8mil spacing
  Stripline: 3.5 mil at 8mil spacing
  Length-matched within +/- 2 mil
  All QSE-to-FMC lines
    3300 mil
    Pass through exactly two vias (from top to signal layer to bottom)
  >20 mil gaps between pairs
  Blind vias
Displayport Lanes & AUX
  AC-coupled per specifications, 100nF X5R/X7R
  Ground plane voids under caps; via clearance + parallel ground vias
Single-ended:
  Nominal 50 ohm, 5mil microstrip & stripline
  >~20 mil spacing between signals
No signals traverse ground plane voids except very short stretches in FMC escapes

## Slide 6: Stackup
Finished size 5.75 x 3.5 inches
Layers 1/3/5/7/(9)/(10) – signal
  L9 contains one differential signal (LA02/ EXP2_DIFF_CLK_OUT), a handful of single-ended signals, and VCC_EXP2_3V3
  L8 contains one leg of +3V3
  L7 is used for 3V3_RX well-away from critical signals
Layers 2/4/6/8/(9)/(10) – GND
FMC escape routing for DP on L8 with large ground pour in L7
According to my calculations, the substrate should have an Er of approximately 3.8 and at least 2110 weave
1oz copper top and bottom, 0.5oz copper inner layers
Most vias are 20mil external diameter/16 mil internal with 8mil drill; ground and power vias use at least a 10mil drill and often larger via diameters

## Slide 7: Miscellaneous Bits
Passive components are mostly 0402 and are all SMD (a few 0603 and 0805 parts)
Caps specified:
  1n, 10n, 100n, 1u: X7R Murata ceramic 25V
  10u: X5R Murata ceramic 6.3V
    I’m ok with solid tantalum or other non-electrolytic caps for these larger values
Resistors are all 0402 Vishay 1% metal film
Reverse-polarity and regulator protection diodes are BAS21W SOT-323-3
  These are rated for continuous 0.2A and surge of 2A; I might upgrade the ones on the main input rails (D300, D305) to 1A-rated diodes
LED indicators on power rails (internal and external 3V3, main 3V3, 1V8, and 3V3_RX)